## Slide 2
COLLABORATION DEVELOPMENT
R&D Plan meeting
collaboration process to support tape-out IC

## Slide 3: Agenda
Design Finalization
Verification Closure
Integration & Signoff
Tape-Out Readiness Review (TOR)
Tape-Out Submission

## Slide 4: 1. Design Finalization
Resource Involved:
  Front-end (RTL design, verification)
  Back-end (physical design, STA)
  DFT (Design-for-Test)
  Power/Clock teams
Tasks:
  Finalize RTL and constraints
  Verify logic functionality (via simulations and formal verification)
  Insert DFT structures (scan chains, BIST)
  Close timing, area, and power budgets

## Slide 5: 2. Verification Closure
Resource Involved:
  Functional Verification
  Formal Verification
  DFT
  Signoff Verification (STA, IR drop, EM, LVS, DRC)
Tasks:
  Full-chip regression tests
  Functional coverage closure
  Formal checks for deadlocks or unreachability
  Physical verification checks:
  LVS (Layout vs Schematic)
  DRC (Design Rule Check)
  ERC (Electrical Rule Check)

## Slide 6: 3. Integration & Signoff
Resource Involved:
  Physical Design
  CAD/EDA Tool Support
  Packaging
Tasks:
  Integrate all blocks into top-level design
  Run signoff timing with foundry libraries
  IR drop and EM analysis
  Final parasitic extraction
  Review of ECO (Engineering Change Orders)

## Slide 7: 4. Tape-Out Readiness Review (TOR)
Resource Involved:
  Project Management
  EDA Tool Experts
  Foundry Interface Team
  QA/Signoff Teams
Tasks:
  Final checklist review
  Tape-out readiness metrics (timing closure, DRC/LVS/antenna clean)
  Approvals from all stakeholders
  Generate GDSII or OASIS file for fabrication

## Slide 8: 5. Tape-Out Submission
Resource Involved:
  CAD/Tooling
  Foundry Interface Team
  Project Management
Tasks:
  Deliver final GDSII/OASIS to the foundry
  Include documentation, test vectors, IP rights
  Foundry submission forms and process compliance
  Confirm successful delivery and receipt by foundry

## Slide 9: 6. Post-Tape-Out Support
Teams Involved:
  Validation/Bring-up
  Test Engineering
  Foundry/Packaging
  Customer/Marketing
Tasks:
  Work with foundry for mask creation and wafer processing
  Initial silicon bring-up and validation
  Yield and failure analysis
  Prepare production test patterns